## Slide 1: CORA
FANG Ji

## Slide 2: Problem
DSP programmers take care of everything
  Algorithm
  Memory
  Scheduling
Code cannot be reused due to high coupling
  algorithm code and control code are mixed together.

## Slide 3: Goal
Design a high performance DSP programming model
Modularized design to improve code reuse
  Separate data flow and control flow
Simplify developing process

## Slide 4: What should a block look like?
Configuration interface
  Set parameters of a block
Algorithm code
  How to process data

## Slide 5: Definition of Block
Variable input channels and variable output channels
Init function
  Config a block
Reset function
  Reset a block
Work function
  Imp. an algorithm
Block
M
N
DEFINE_BLOCK(sample_block, 1, 1)
{
BLOCK_INIT
{
auto v = $["nTaps"];
}
BLOCK_WORK
{
auto in = _$<int>(0);
auto out = $_<int>(0);
……………..// do something
consume(0, n);
produce(0, m);
return true;
}
};
autoref spblk = create_block<sample_block>(2, string("nTap=10"), string("nCount=20"));

## Slide 6: Memory Model
Local variable
  _local_(type, name, initial);
Global variable
  _global_(type, name);
_local_(int, a, 0);
_global_(int, g);
Block A
_local_(int, a, 0);
_global_(int, g);
Block B
a
a
g

## Slide 7: Execution model
Blocks communicate via unbounded FIFO channels.
Blocks read and write data elements from and to channels.
  Writing to a channel is non-blocking, i.e. it always succeeds and does not stall the process
  Reading from a channel is blocking, i.e. a process that reads from an empty channel will stall and can only continue when the channel contains sufficient data items.
  Depth first, sink first
Notes: Kahn Process Networks

## Slide 8: Control flow
Determines the scheduling sequences of connected blocks
Primitives
  START, STOP, ONCE, ONCEIF, IF, IFNOT, ELSE_IF, ELSE
    START(A, B, C,…,X);
    STOP(finalization_code)
    ONCE(A, B, C,…,X);
    ONCEIF(A, B, C,…,X);
    IF(condition)  if ( condition )
    IFNOT(condition)  if ( ! condition )
    ELSE_IF(condition)  else if ( condition )
    ELSE  else
  A, B, C… and condition can be any functor or function or lambda function which take no parameter and return bool value;
    i.e., bool X(){ return true;}
  Implemented as templates to enable compile time code optimization

## Slide 9: Control flow (cont.)
Sequential flow
A
B
C
D
START(A, B, C, D); 
  while ( A() ) while ( B() ) while ( C() ) while ( D() );

## Slide 10: Control flow (cont.)
Branch flow
START(A, B, IF(C), F, G, ELSE_IF(D), H, I, ELSE, J );
A
B
F
G
H
I
J
IF(C)
ELSE_IF(D)
ELSE

## Slide 11: Control flow (cont.)
Multiple output flow
START(A, B, [&]{ START(C, D);
START(E, F); }
);
A
B
C
E
F
D

## Slide 12: Control flow (cont.)
Loop flow
START(A, B, C, D);
START( A, [&]{START(B); START(C, D);} );
A
B
C
D
A
C
D
B

## Slide 13: Control flow (cont.)
Compile time dynamic code generation
START(A, B,…X) as a template function
  Each parameter is marked by an OP function
    while, if, else_if, else
  __if_exist(A::while){ while(A()) }
  __if_exist(A::if){ if(A()) }
  __if_exist(A::else_if){ else if(A()) }
  __if_exist(A::else){ else }

## Slide 14: Primitive: STOP
Stop a control flow and execute the finalization code
  START(A, B, IF(C), STOP( [&]{ // finalization code here }) );

## Slide 15: Primitive: STOP
START(src, IF([&]{return status==0;}), [&]{ START(acorr, IF(stf), STOP([&]{status=1;})); }, ELSE_IF([&]{return status==1;}), [&]{ START(foe);} );
src
acorr
int status = 0;
stf
7 v_cs
1 v_cs
4 int64
4 int64
foe
status:0
status:1
What’s your scheduling code ?

## Slide 16: Primitive: ONCE & ONCEIF
ONCE(A, B, C,…,X);
  Execute each block once one by one no matter the return value.
  i.e.
    A(); B(); C(); … X();
ONCEIF(A, B, C,…,X);
  Execute each block once if previous block returns true.
  i.e.
    if ( A() ) if ( B() ) if ( C() ) … if ( X() ) ;

## Slide 17: Primitive: ONCE
Example:
  Assembly line
    ONCE(A, B, [&]{START(C);});
  802.11g TX flow
    ONCE(add_stf, add_ltf, [&]{START(conv_12, intl, map_bpsk, fft, GI, …);} ,//add_sig [&]{START(conv_23, intl, map_qpsk, fft, GI, …);}//add_data );
A
B
C
A
B
C
C
C
…
+

## Slide 18: Primitive: ONCE
Multiple blocks work on the same data
  ONCE(RmGI, FFT, ChComp, Pilot, Demap, …);
RmGI
FFT
Pilot
ChComp
Demap
Part of 802.11g RX baseband

## Slide 19: Channel
Blocks communicate via channels.
  Modeled as Single Writer Multiple Reader buffer
A channel may have 1+ writers/readers
  Only 1 writer is permitted to write data at a time
  Only 1 shared reader is permitted to read data at a time
  1+ independent readers can read data simultaneously
A
B
C
D
E
G
F
  Channel::Create(sizeof(v_cs)) .from(A, 0).from(B, 0) .to(C, 0).to(D, 0).to(E, 0)
  .to(F, 0, false).to(G, 0, false);

## Slide 20: Creating Data Flow Graph
Create blocks
  autoref src = create_block<b_file_source>();
  autoref awgn = create_block<b_awgn>();
  autoref sink = create_block<b_file_sink>();
Create channels & connect to blocks
  Channel::Create(sizeof(v_cs)) .from(src, 0) .to(awgn, 0);
  Channel::Create(sizeof(v_cs)) .from(awgn, 0) .to(sink, 0);
src
awgn
sink

## Slide 21: 802.11n TX
L_STF
DMA
Join
L_LTF
L_SIG
conv12
interlv
BPSK_i
Pilot
IFFT
CP
CSD
CP
HT_SIG
HT_STF
HT_LTF
HT_DATA
conv
interlv
map
BPSK_q
SP
interlv
map
IFFT
IFFT
Pilot
Pilot
CP
CSD
CP
scramble

## Slide 22: 802.11n RX
src
Auto corr
LSTF
CFE
CFO
FFT
SISO
CHE
RM GI
FFT
SISO
CHC
MRC
demap
deintlv
viterbi
Lsig
parser
RM GI
FFT
SISO
CHC
MRC
demap
deintlv
viterbi
htsig
parser
HT STF
RM GI
FFT
RM GI
FFT
MIMO
CHE
MIMO
CHO
Demap
Deintlv
join
Viterbi
Descramble
CRC32
L_SIG
HT_SIG
HT_DATA
HT_LTF
L_STF
L_LTF
HT_STF

## Slide 23: Roadmap
Design & preliminary imp. 2 w
Sequential primitives 1w
802.11n RX 1 w
Parallel & async primitives
802.11n TX 1 w

## Slide 24: Perf.
8 | 9 | 10 | 11 | 12 | 13 | 14
33.653971 | 62.351629 | 89.538893 | 100.5674 | 139.97304 | 155.87907 | 170.61391
8 | 9 | 10 | 11 | 12 | 13 | 14
44.911475 | 26.520226 | 19.195442 | 12.640718 | 10.477418 | 7.293792 | 7.161673
TX: (Mbps)
RX: (Msps)
Chart: Encoding Throughput(Mbps)
| 8 | 9 | 10 | 11 | 12 | 13 | 14
8 | 33.654
9 | 62.3516
10 | 89.5389
11 | 100.5674
12 | 139.973
13 | 155.8791
14 | 170.6139
Chart: Decoding Throughput(Msps)
| Rate
8 | 44.9115
9 | 26.5202
10 | 19.1954
11 | 12.6407
12 | 10.4774
13 | 7.2938
14 | 7.1617
i7-980X (6 cores, 3.33GHz), 8G 1333 RAM

## Slide 25: Thanks! Q&A

## Slide 26: Backup

## Slide 27: Unbounded FIFO
Implementation
0
N-1
N
2N-1
Virtual address
Physical address

## Slide 28
CP
CSD
CP
HT_DATA
interlv
map
interlv
map
IFFT
IFFT
Pilot
Pilot
scramble
conv
conv
scramble
MCS | CONV | INTERLV | Rate Match
8(BPSK, 1/2) |  | 6.5 (Re Imp.) | 13
9(QPSK, 1/2) |  | 13 | 26
10(QPSK, 3/4) |  | 13 | 39
11(16QAM, 1/2) |  | 26 | 
12(16QAM, 3/4) |  | 26 | 
13(64QAM, 2/3) |  | 39 | 
14(64QAM, 3/4) |  | 39 | 

## Slide 29
CP
CSD
CP
HT_DATA
interlv
map
interlv
map
IFFT
IFFT
Pilot
Pilot
scramble
conv
conv
scramble
6.5->1
13->2
52->4
1->2
2->4
26->52
26
MCS8
MCS9
1->2
13->26
13->1
26->2
MCS10
13
3->4
39->52
13->1
52->4
39